Benchmarks: Pipelines

---
Benchmarks: Goals
- Typical telco pipelines
- Can be coded into most of our switches/data-planes (with documented restrictions)
- Allow realistic dynamic workloads (add/del entries to/from flow table)
- Performance illustrative in general
- Currently BESS and OVS are to be supported (with prefab the pipeline config), Lagopus and ERFS should be added (Vpp would be very difficult)

---
Benchmarks: Pipelines
- Macro-benchmarks:
  - Mobile gateway (5G?) – more or less ready
  - Broadband Network Gateway (BNG) – work-in-progress
- Micro-benchmarks: what is a micro-benchmark after all?
- Possible (not so) micro-benchmarks:
  - port forward
  - L2
  - L3
  - encap/decap
  - ????

---
Mobile Gateway
Put users behind the base stations (bsts) to the Internet
Mobile Gateway, different UL/DL
UL (from UE): GTP encapsulated packets
L2, L3 and L4 check (GW, UDP, 2152)
GTP decaps, save TEID
rate limit per bearer (TEID)
L3 routing towards Internet + L2 fwd
DL (to UE): normal IP packets
L2 and L3 check (DstIP is in UE range)
DstIP -> rate limit + GTP encaps + set ext DstIP
L3 routing towards BSTs + L2 fwd
Traces:
Uplink: 10k GTP packets from 100 Base Stations (BSTs)
external: DstIP = GW, DMAC = GW, SrcIP = BST(i)
internal: DstIP = server (1k), SrcIP = UE (10k)
Downlink: 10k IP packets, SrcIP = server, DstIP = UE
packet sizes:
64, 128, 256, 512, 1024, 1280
filenames:
TBD
Configuration
before test
use traces + next slide
set S/DMAC
set IP addresses + TEIDs
use same TEIDs UL/DL
do not do fragmentation (limit MTU)
routes should match traffic
Tests:
2 x uni + bi-directional
1-2-4-8-… cores
64-1280 byte packets
to avoid fragmentation
(if needed we can test it later)
In: physical 10/40/100G
Out: physical 10/40/100G

---
Mobile Gateway: Static config
- Uplink: GTP decap→rate-limit→L3 lookup→group
- Downlink: id user→GTP encap→L3 lookup→bst
Rate limiter #1
Rate limiter #1
Ethertype
key: Ethertype
entries: 2
L3 fwd block
(see L3 fwd case)
type = 0x0806 (ARP)
own MAC + broadcast
ARP to GW IP
answer: Own MAC
Infra CP
L2 fwd block
(see L2 fwd case)
IP + UDP select
key: IP.dst, UDP dport
entries: 2
GTP handler
(pop GTP, save TEID)
UL: GW IP, UDP, 2152
DL: DstIP in UE range
Rate limiter #i
key: TEID
UE selector
key: IP.dst
type: Hash
entries: 10k
actions: push GTP, set IP
out
port

---
BESS: Considerations
- Egress/ingress traffic mapped to a single physical port; drop port configurable, either to default port (for rate measurements), or real drop port
- No GTP in BESS: substituted with VxLAN
- Rate limiters in BESS: no rate limiter per se, emulated with a Queue + Scheduler
- Uplink/downlink go through a single per-user rate limiter: currently downlink rate limiting is for packets with VXLAN header, downlink for packets without VXLAN header

---
BESS: Considerations
Scheduling: the pipeline is scheduled from the input port and runs in run-to-completion mode, with users' queues separately
$ show tc
<worker 0>
  +-- !default_rr_0 round_robin
      +-- t_0_0 rate_limit 100000.000 Mbps
      | +-- !leaf_rl_0_0:0 leaf
      +-- t_0_1 rate_limit 100000.000 Mbps
      | +-- !leaf_rl_0_1:0 leaf
      +-- t_0_2 rate_limit 100000.000 Mbps
      | +-- !leaf_rl_0_2:0 leaf
      +-- !leaf_queue_inc0:0 leaf
3 users, users' queues (t_0_?) are rate limited
scheduled together with the input queue in round-robin

---
BESS pipeline
INGRESS:
EGRESS:
Rate limiters (per user)
L3 fwd block
L3 lookup
group entries
uplink groups
downlink groups

---
BESS pipeline
UPLINK:
INGRESS
EGRESS
DOWNLINK:
INGRESS
EGRESS

---
OVS: Considerations
- Egress/ingress traffic mapped to a single physical port; drop port configurable, either to default port (for rate measurements), or real drop port
- OpenFlow 1.3: should be supported by OVS, Lagopus, ESwitch/ERFS
- GTP→VXLAN: to be on par with the BESS pipeline
- VXLAN via standard OpenFlow “virtual port” abstraction (OXM_OF_TUNNEL_ID): no need to explicit encap/decap but we lose OpenFlow compatibility (Lagopus/ERFS??)
- Rate limiters: per user OpenFlow “meters”

---
OVS pipeline
uplink: per-user rate limiters→L3
in_port=vport1, tunnel_id=user1(bst1), action: meter(user1(bst1)), goto:L3
in_port=vport1, tunnel_id=user2(bst1), action: meter(user2(bst1)), goto:L3
...
in_port=vport1, tunnel_id=useri(bst1), action: meter(useri(bst1)), goto:L3
in_port=vport2, tunnel_id=user1(bst2), action: meter(user1(bst2)), goto:L3
...
vport 1: bst1↔gw
Group1
Group1
vport 2: bst2↔gw
Group2
L3 lookup
(srvs)
vport k: bstk↔gw
Groupn
downlink: per-user rate limiters→vport for the proper bst
dst_ip=IP(user1), action: set_tunnelLteid(user1), meter(user1),output:vport(user1)
dst_ip=IP(user1), action: set_tunnelLteid(user1), meter(user1),output:vport(user1)
...
phys port

---
Dynamic workloads
- Goal: measure impact of flow table changes to performance
- Scenarios:
  - handover (user changes base station)
  - user add/delete: users disappear/appear
  - server changes (L3 destination entries change)
- Considerations:
  - change rate: perform the entire change in one shot every second (in one batch)
  - dynamism: add/delete the same entry (e.g., user comes, same user leaves)
- BESS: from bess config script, OVS: from Ryu

---
How to use
Clone git tree: TODO
1. Generate config (10 users, 5 servers, 5 bsts, 4 handovers/sec, 5 usermods/sec)
2. Generate pcaps (200 thousand packets, each of 100 bytes, uplink+downlink, ASCII dump)
3. (Optionally) start flow table modification scripts
4. Start measurement (manually)
$ gen_scripts/mgw-gen-conf.py -u 10 -s 5 -b 5 --handovers 4 --fluctusers 5 -o mgw-updates.json
$ gen_scripts/mgw-gen-pcap.py -c mgw-updates.json --pkt-num=200000 --pkt-size 100 -a --dir b

---
BNG
TODO